## Slide 1: Scientific Machine Learning for Modeling, Optimization, and Control of Dynamical Systems
Ján Drgoňa
Associate Professor Civil and Systems Engineering Department The Ralph O'Connor Sustainable Energy Institute (ROSEI)
Data Science and AI Institute (DSAI)

## Slide 2: Course Syllabus
Week 1: Introduction to Scientific Machine Learning (SciML)
Week 2: Preliminaries and Introduction to differentiable programming
Week 3: Physics-informed neural networks (PINNs)
Week 4: Neural ordinary differential equations (NODEs)
Week 5: Learning to optimize (L2O)
Week 6: Optimal control preliminaries
Week 7: Learning to control (L2C)
Week 8: Feasibility restoration methods in L2O
Week 9: Neural differential equations with constraints
Week 10: Safety filters for L2C
Week 11: Predict then optimize: decision focused learning
Week 12: Project evaluation with presentations
Week 13: Project evaluation with presentations

## Slide 3: Learning to Control (L2C)
Nghiem T., Drgona J., et al. Physics-Informed Machine Learning for Modeling and Control of Dynamical Systems, ACC, 2023.
J. Drgoňa et al., "Safe Physics-informed Machine Learning for Dynamics and Control," 2025 American Control Conference (ACC), 2025.

## Slide 4: Learning to Control (L2C) Applications
Trajectory optimization for dynamical systems
Quadcopter control
Chemical process control
Robotics path planning and control

## Slide 5: Learning to Control Problem Formulation

## Slide 6: L2C Policy Representation
James Kotary, My H. Dinh, Ferdinando Fioretto, Backpropagation of Unrolled Solvers with Folded Optimization, IJCAI, 2023

## Slide 7: L2C Methodologies
Supervised L2C: Approximate Model Predictive Control
Self-Supervised L2C: Differentiable Predictive Control (DPC)
J. Drgoňa, A. Tuor and D. Vrabie, "Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees," in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
Ján Drgoňa, et al, Differentiable predictive control: Deep learning alternative to explicit model predictive control for unknown nonlinear systems, Journal of Process Control, 2022
M. Hertneck, et al., "Learning an Approximate Model Predictive Controller With Guarantees," in IEEE Control Systems Letters, 2018
B. Karg and S. Lucia, "Efficient Representation and Approximation of Model Predictive Control Laws via Deep Learning," in IEEE Transactions on Cybernetics, 2020

## Slide 8: Supervised L2C: Approximate MPC
Step 1: solve set of MPC problems to generate labeled training data
Step 2: supervised imitation learning to learn approximate MPC policy
M. Hertneck, et al., "Learning an Approximate Model Predictive Controller With Guarantees," in IEEE Control Systems Letters, 2018

## Slide 9: Supervised L2C Loss Function and Dataset
This is equivalent with supervised L2O method.

## Slide 10: Self-Supervised L2C: Differentiable Predictive Control (DPC)
J. Drgoňa, A. Tuor and D. Vrabie, "Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees," in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
Dataset: collocation points in the control parametric space.
Loss function: reference tracking, constraints and terminal penalties.
Architecture: differentiable model with neural network control policy.
https://github.com/pnnl/neuromancer/blob/master/examples/control/Part_3_ref_tracking_ODE.ipynb

## Slide 11: DPC Problem Formulation

## Slide 12: DPC Loss Function and Dataset

## Slide 13: Differentiable Closed-Loop System

## Slide 14: Differentiable Closed-Loop System

## Slide 15: DPC Policy Optimization Algorithm

## Slide 16: DPC Assumptions

## Slide 17: DPC vs Model-based Reinforcement Learning
J. Drgoňa, A. Tuor and D. Vrabie, Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees, in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
J. Drgoňa, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
DPC is closely related to MBRL in that both leverage model of dynamics, but DPC utilizes differentiable closed-loop models and cost functions, allowing direct policy gradients without requiring a learned critic.
Empirical risk minimization problem:
Policy gradient via automatic differentiation:
Critic parametrized by differentiable MPC-like loss function:

## Slide 18: DPC vs Model Predictive Control
J. Drgoňa, A. Tuor and D. Vrabie, Learning Constrained Parametric Differentiable Predictive Control Policies With Guarantees, in IEEE Transactions on Systems, Man, and Cybernetics: Systems, 2024
J. Drgoňa, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
DPC is also related to explicit MPC, as it solves a parametric optimal control problem via gradient-based policy optimization.
There is a structural equivalence between single shooting formulation of MPC problem and the unrolled closed-loop system dynamics in DPC.
DPC is also closely related to MPC, but instead of single instance online optimization, the DPC learns parametric explicit policy offline, over distribution of parametric instance.

## Slide 19: DPC Advantages

## Slide 20: DPC Disadvantages

## Slide 21
github.com/cvxpy/cvxpylayers
github.com/pnnl/neuromancer
Learning to Control Libraries
https://github.com/MaxMSun/lqrax
www.do-mpc.com/en/latest/index.html

## Slide 22: DPC in NeuroMANCER Scientific Machine Learning Library
github.com/pnnl/neuromancer
DPC Examples
Learning to stabilize a linear dynamical system
Learning to stabilize a nonlinear differential equation.
Learning to control a nonlinear differential equation.
Learning neural ODE and control policy for an unknown dynamical system.
Learning neural Lyapunov function for a nonlinear dynamical system.
Mixed-Integer DPC

## Slide 23: Homework Assignment: Project Proposal
Project proposal: Who did not score 100 points, update your proposal based on the feedback.
The proposal must include following paragraphs:
Summary: Single sentence providing concise overview of the proposal.
Introduction: Provides context and problem statement. Answers what is the problem and why is the problem important.
Objectives: States clear and specific objectives of the proposal. Answers what we want to achieve.
Technical approach: Detailed explanation of how the project will be executed. Provides steps, strategies, and techniques to be used. Answers how are we going to achieve our objectives.
Expected outcomes: Key results expected from the project. Performance indicators and success metrics.

## Slide 24: Week 11: Project Presentations and Evaluation
Projects cover 70% of the course grade!
  Project proposal 20% - week 5
  Project progress report 10% - week 8
  Project final report 20% - week 10
  Project presentation 20% - week 11
Project format.
      Project technical report: 4 to 6 page long pdf document including references and figures.
  Project presentation: ppt or pdf slides, 15 min time slot per student in week 11.
Admissible topics.
      Application of selected SciML methods to problems inspired by real-world applications
        e.g., L2O for large scale optimization of energy systems.
      Development of new methods tackling some of the open challenges in SciML
        e.g., novel way of utilizing PINNs in differentiable control for PDEs.
      New theory supporting selected SciML methodology
        e.g., convergence analysis of feasibility restoration layers in L2O.